## Slide 1
NFC TECHNOLOGY
Smartdev Mobile Team
Presenter: Hoang Ngoc Tan

## Slide 2
NFC Basic
Part 1
NFC Protocol (APDU)
Part 2
Read an NFC Card
Part 3
Simulate an NFC Card
Part 4
Contents

## Slide 3
NFC Basic
Part 1
NFC Protocol (APDU)
Part 2
Read an NFC Card
Part 3
Simulate an NFC Card
Part 4
Contents

## Slide 4
NFC Basic
Benefits
The benefit of NFC
02
Defination
What is NFC technology?
01
Usage
The usage of NFC
03
Basic Concepts
Some concepts
04
NFC Detection
How to detect if device has NFC available?
05

## Slide 5
1. What is NFC?
Near Field Communication
short range high frequency wireless communicaton technology
Radio Communication
established by touching the two phones or keeping them in a proximity of a few centimeters (up to 10 cm)
Communication mode
Card Emulation
Enables NFC-enabled devices such as smartphones to act like smart cards, allowing users to perform transactions such as payment or ticketing
Card Reader/ Writer
Enables NFC-enabled devices to read information stored on inexpensive NFC tags embedded in labels or smart posters
peer-to-peer
Enables two NFC-enabled devices to communicate with each other to exchange information
Communication Type
Active communication
(2 powered NFC devices)
Passive communication
(1 powered NFC device & 1 non (self) powered device)

## Slide 6
2. Benefit of NFC?
Convenience
Security
SmartCard using Secure Element
(a tamper resistant smart card chip capable of running smart card applications (called applets or cardlets) with a certain level of security and features)
Short range communication
(hard to stolent the transfering data)

## Slide 7
3. NFC Usage
Mobile transactions
Access Information
Connect Electronic Devices
Contactless payment
Mobile
ticketing
  Advertisements
  Identification Cards
  Control IOT device

## Slide 8
4. Basic concepts
NFC Tags
NDEF
NFC Data Exchange Format
APDU
Application Protocol data unit
APDU command
NDEF message
Applet
Secure element
tag
Tag
tag
tag

## Slide 9
4. Basic concepts
NFC TAGS
passive data stores
- contain data (betweens 96 and 8,192 bytes).
- are read-only in normal use, but may be rewritable
- can be read, and under some circumstances written to, by an NFC device.
secure personal data storage
- includes debit or credit card information, loyalty program data, personal identification numbers (PINs), contacts.
- NFC tags can be custom-encoded by their manufacturers or use the industry specifications.

## Slide 10
4. Basic concepts
NDEF – NFC Data Exchange Format
NDEF messages provide a standardized method for a reader to communicate with an NFC device
contains multiple records

## Slide 11
4. Basic concepts
APDU – Application Protocol Data Unit
The communication unit between a smart card reader and a smart card
The structure of the APDU is defined by ISO/IEC 7816-4

## Slide 12
4. Basic concepts
Applet – Application Protocol Data Unit
The communication unit between a smart card reader and a smart card
The structure of the APDU is defined by ISO/IEC 7816-4

## Slide 13
NFC Basic
Part 1
NFC Protocol (APDU)
Part 2
Read an NFC Card
Part 3
Simulate an NFC Card
Part 4
Contents

## Slide 14
APDU
Command APDU
00 A4 04 00 0E32 50 41 59 2E 53 59 53 2E 44 44 46 30 31 00
6F 39 84 0E 32 50 41 59 2E 53 59 53 2E 44 44 46 30 31 A5 27 BF 0C 24 61 22 4F 07 A0 00 00 00 03 10 10 50 10 56 43 42 20 56 49 53 41 20 50 41 59 57 41 56 45 87 01 01 9F 2A 01 03 90 00
Response APDU

## Slide 15
APDU
Command APDU

## Slide 16
APDU
Command APDU
00 A4 04 00 0E32 50 41 59 2E 53 59 53 2E 44 44 46 30 31 00
Select PPSE command

## Slide 17
APDU
Command APDU

## Slide 18
APDU
Command APDU
Select PPSE response explanation

## Slide 19
APDU
Command APDU
Smart Cart Commands & Response codes reference:
http://www.wrankl.de/SCTables/SCTables.html

## Slide 20
NFC Basic
Part 1
NFC Protocol (APDU)
Part 2
Read an NFC Card
Part 3
Simulate an NFC Card
Part 4
Contents

## Slide 21
Build a Card Reader
1/ Request NFC access
2/ Filter for NFC intent (optional)
3/ Implement NfcAdapter
4/ Process the APDU command
Read an NFC Card

## Slide 22
Build a Card Reader
1. Request NFC access
Permission to access the NFC hardware
The NFC <uses-permission> element to access the NFC hardware
Tell Google Play that only show your app for devices that have NFC hardware
<uses-permission android:name="android.permission.NFC"/>
<uses-feature android:name="android.hardware.nfc.hce" android:required="true"/>

## Slide 23
Build a Card Reader
2. Filter for NFC intent (optional)
Register a filter
The NFC <uses-permission> element to access the NFC hardware
Specify the kind of tech that
our application want to handle
<intent-filter> <action android:name="android.nfc.action.TECH_DISCOVERED"/> </intent-filter> <meta-data android:name="android.nfc.action.TECH_DISCOVERED" android:resource="@xml/nfc_tech_filter" />
<?xml version="1.0" encoding="utf-8"?> <resources xmlns:xliff="urn:oasis:names:tc:xliff:document:1.2"> <tech-list> <tech>android.nfc.tech.IsoDep</tech> </tech-list> <tech-list> <tech>android.nfc.tech.NfcA</tech> </tech-list> <tech-list> <tech>android.nfc.tech.NfcB</tech> </tech-list> </resources>

## Slide 24
Build a Card Reader
3. Implement NFC Adapter
Initiate an NfcAdapter
The NFC <uses-permission> element to access the NFC hardware
Enable adapter Reader mode
nfcAdapter = NfcAdapter.getDefaultAdapter(this)
nfcAdapter?.enableReaderMode(this, this, NfcAdapter.FLAG_READER_NFC_A or NfcAdapter.FLAG_READER_SKIP_NDEF_CHECK, null)
Implement Reader callback
override fun onTagDiscovered(tag: Tag?) { val isoDep = IsoDep.get(tag) isoDep.connect() processAPDUCommands(isoDep) isoDep.close() }

## Slide 25
Build a Card Reader
4. Process the APDU command to read Card data
Defines Apdu commands
The NFC <uses-permission> element to access the NFC hardware
Executes the commands
val apduCommandMap: Map<String, String> = mapOf( "SELECT_AID" to "00A4040007A000000003101000", "GET_PROCESSING_OPTIONAL" to "80A80000238321278xxxxxx00", "GET_PIN_TRY_COUNTER" to "80CA9F1700", "GET_TRANSACTION_COUNTER" to "80CA9F3600" )
fun executeApduCommand(apduCommandString: String, isoDep: IsoDep): ByteArray { return isoDep.transceive(TypeConvertor.hexStringToByteArray(apduCommandString)) }

## Slide 26
NFC Basic
Part 1
NFC Protocol (APDU)
Part 2
Read an NFC Card
Part 3
Simulate an NFC Card
Part 4
Contents

## Slide 27
1/ Host-base card Emulation
2/ Build a Smartcard simulator
Simulate an NFC Card

## Slide 28
Card emulation with a secure element
Host-based card emulation
Simulate an NFC Card
1. Host-base card Emulation
data is routed directly to the secure element
no Android application is involved in the transaction
data is routed directly to the host CPU

## Slide 29
Requires
Android 4.4 or higher
Simulate an NFC Card
1. Host-base card Emulation
ISO-DEP specification (based on ISO/IEC 14443-4)
Nfc-Type: Nfc-A (on top), Nfc-B (optional)
Application Protocol Data Units (APDUs) as defined in the ISO/IEC 7816-4 specification

## Slide 30
Implement an HCE service
Simulate an NFC Card
2. Build a Smartcart Simulator
Check for HCE support
Declare a Host apdu service
Specify the Aid filter
Handle process Command apdu received from the Terminal

## Slide 31
Check for HCE support
Simulate an NFC Card
2. Build a Smartcart Simulator
declare that your app uses the HCE feature, and whether it is required for the app to function or not
<uses-feature android:name="android.hardware.nfc.hce" android:required="true"/>

## Slide 32
Declare a Host apdu service
Simulate an NFC Card
2. Build a Smartcart Simulator
service android:name=".service.HostCardEmulatorService" android:exported="true" android:permission="android.permission.BIND_NFC_SERVICE"> <intent-filter> <action android:name="android.nfc.cardemulation.action.HOST_APDU_SERVICE"/> </intent-filter> <meta-data android:name="android.nfc.cardemulation.host_apdu_service" android:resource="@xml/apduservice"/> </service>

## Slide 33
Specify the Aid filter
Simulate an NFC Card
2. Build a Smartcart Simulator
<host-apdu-service xmlns:android="http://schemas.android.com/apk/res/android" android:description="@string/servicedesc" android:requireDeviceUnlock="false"> <aid-group android:description="@string/aiddescription" android:category="other"> <aid-filter android:name="A0000000031010"/> <!-- Indicate that the service will only handle the request to the aid VISA DEBIT = A0000000031010--> </aid-group> </host-apdu-service>

## Slide 34
Handle process Command apdu received from the Terminal
Simulate an NFC Card
2. Build a Smartcart Simulator
class HostCardEmulatorService: HostApduService() { override fun processCommandApdu(commandApdu: ByteArray?, p1: Bundle?): ByteArray { val commandApduStr = TypeConvertor.toHex(commandApdu)
handleApduRequest() } override fun onDeactivated(reason: Int) { Log.d(TAG, "HostCardEmulatorService Deactivated: " + reason) } }

## Slide 35
Thank all !